## Slide 1: Signals and Systems Lecture 4 Zero-state response
DR TANIA STATHAKI
READER (ASSOCIATE PROFFESOR) IN SIGNAL PROCESSING IMPERIAL COLLEGE LONDON

## Slide 2: The importance of impulse response
Zero-state response assumes that the system is in “rest” state, i.e. all internal system variables are zero.
Deriving and understanding the zero-state response relies on knowing the so called unit impulse response
Definition: The unit impulse response is the system’s response when the input is the Dirac function, i.e., , with all the initial conditions being zero at .
Any input can be broken into a sequence of narrow rectangular pulses. Each pulse produces a system response.
If a system is linear and time invariant,
the system’s response to is the sum of its
responses to all narrow pulse components.
is the system’s response to the rectangular
pulse at as the pulse width approaches zero.

## Slide 3: How to determine the unit impulse response ?
Given that a system is specified by the following differential equation, determine its unit impulse response .
,
Remember the general equation of a system:
It can be shown (proof is out of the scope of this course) that the impulse response is given by
where is the unit step function. But what is ?

## Slide 4: How to determine the unit impulse response ?
is the solution to the homogeneous differential equation (what we called in the previous lecture)
with the following initial conditions:
,
We use instead of to associate with the specific set of initial conditions mentioned above.
Remember that is a linear combination of the characteristic modes of the system.
The constants are determined from the initial conditions.
Note that is the th derivative of at .

## Slide 5: Example
Determine the impulse response for the system:
This is a second-order system (i.e., ) and the characteristic polynomial is:
The characteristic roots are and .
Therefore, .
Differentiating the above equation yields .
The initial conditions are and .

## Slide 6: Example cont.
Setting and substituting the initial conditions yields:
The solution of the above set of equations is:
Therefore, we obtain:
Remember that is given by:
with in this case.
Therefore:
[Note that: ]

## Slide 7: Zero-state response
Consider a linear, time-invariant system with impulse response .
The output at time due to a shifted impulse with amplitude located at time instant is the impulse amplitude multiplied by a shifted impulse response located at as well.
In other words:
If we generalize the above observation we can say that the output of a linear system to an input is
Linear System

## Slide 8: Zero-state response cont.
We now consider how to determine the system’s response to any input when the system is in the zero state (initial conditions are zero).
Define a pulse of height equal to 1 and width starting at (see top figure on the right).
Any input can be approximated by a sum of narrow and shifted rectangular pulses.
The pulse starting at has a height .
It can be expressed as
Therefore, is approximated by the sum of all such pulses as follows:
or

## Slide 9: Zero-state response cont.
The term represents a pulse with height .
As , the height of the pulse
and the width of the pulse
but the area remains and
.
Therefore,

## Slide 10: Zero-state response cont.
Given the relationship and the fact that the system is linear, time-invariant, we have:

## Slide 11: Zero-state response cont.
Based on the previous analysis, the input-output relationship of an LTI system as a function of the impulse response is shown below.

## Slide 12: Zero-state response cont.
Therefore,
Knowing , we can determine the response to any input .
Observe the all-pervasive nature of the system’s characteristic modes, which determines the impulse response of the system.
LTI System

## Slide 13: The convolution integral
The previously derived integral equation occurs frequently in physical sciences, engineering and mathematics.
It is given the name the convolution integral.
The convolution integral (known simply as convolution) of two functions and is denoted symbolically as .
This is defined as

## Slide 14: Convolution properties
Commutative property: The order of operands does not matter.
Let . In that case and and .
Therefore,
Associative property
Distributive property

## Slide 15: Convolution properties cont.
Shift property
Consider
Then
Furthermore,
Convolution with an impulse: The convolution of a function with the unit impulse function is the function itself. Therefore, the unit impulse function acts as an identity (neutral) element for convolution.

## Slide 16: Convolution properties cont.
Width (duration) property: Consider two functions and with durations and respectively.
Then, the duration of the convolution function is
Causality property: If both system’s impulse response and input are causal then:

## Slide 17: Example
For an LTI system with unit impulse response determine the response for the input .
By definition we have:
Since for and for , we see that if which also makes sense only if .
Therefore,
,
Therefore,

## Slide 18: Example cont.

## Slide 19: Relation to other courses
Convolution has been introduced last year in the Signals and Communications course. We will emphasize into convolution and its physical implication in the next lecture.
Zero-state response (as determined through the convolution operation) is very important, and is intimately related to the zero-input response and the characteristic modes of the system.
All these are relevant to the 2nd year Control course.
You will also come across convolution again in your 2nd year Communications course and third year DSP course.